## Slide 1: VG100 Summer 2017 Introduction to Engineering T2: Project 1 – Maze Robot
Yu Zheng, Ph.D. Assistant Professor
University of Michigan-Dearborn
Acknowledge: Lectures include slides prepared by Profs. Jason Daida,
Peisen Huang, Shane Johnson, Thomas Hamade, and Mian Li

## Slide 2: Outline
Project Overview
Major Components Provided
Programming
Project Grading

## Slide 3: Place & Time
Lab: JI General Engr. Lab 1 (4F)
Time:
  Session 1: Wednesday, 16:00-17:40
  Session 2: Tuesday, 12:10-13:50
Final Test: June 13, Tuesday
Game Day: June 14, Wednesday

## Slide 4: Lab Schedule
Week 2: Lecture and practice on Arduino
Week 3: Sensors and motors, prototype (only Wednesday, all teams)
Week 4: Mechanical & electrical prototype
Week 5: Final test and Game day (All teams)

## Slide 5: Maze Robot
Robot
Maze
  Straight and curved path
  Signs showing the directions
  Only 90-degree turns

## Slide 6: Maze Parameters
Straight
Left-turn
Right-turn
U-turn
Round left-turn
Round right-turn
T-junction
Road width: about 30 cm

## Slide 7: Arrow Size
10 cm
5 cm

## Slide 8: What Does the Robot look like

## Slide 9: Components Provided

## Slide 10: Components NOT Provided
Ball caster
Servo motor
Ultrasonic Distance Sensor
Infrared Distance Sensor
Camera

## Slide 11: System Configuration

## Slide 12: Arduino Uno
USB port
Power input
Analog in
Digital I/O
Serial port

## Slide 13: Motor Driver

## Slide 14: Open-Loop Control
An open-loop control system is controlled directly, without using feedback to adjust the process
Pros: simple, low cost, reliable
Cons: low accuracy, sensitive to noise and disturbance, not robust

## Slide 15: Closed-Loop (Feedback) Control
A closed-loop control system uses feedback to adjust the process for better system performance
Pros: high accuracy, robust performance, disturbance rejection, better dynamic response
Cons: higher cost, potential instability problem

## Slide 16: Feedback Control - Example
Temperature control in an oven
  Preheat the oven to 350°F
  Temperature sensor monitors the temperature in the oven
  Turn the heater on if the temperature is below the set temperature
  Turn it off otherwise

## Slide 17: Feedback Control - Example
Mobile robot
  Start the motors to drive the robot
  Sensors monitor the direction
  Adjust the speed and direction of the left and right motors to adjust driving direction
Sensors
Robot

## Slide 18: What Does the MCB Do?
Read signals from external sensors
Send signals to control the DC motors
Execute the control program stored in the on-board memory
Display messages during program execution
Interface to the computer via USB for program download
MCB is the brain of a robot!
Microcontroller Board (MCB) - Arduino Uno

## Slide 19: Motor, Gearbox, and Tire

## Slide 20: Gearbox and its Function
Connect to motor
Connect to tire

## Slide 21: Distance Sensors
Ultrasonic Distance Sensor
Infrared Distance Sensor
Measure time
Measure phase
Triangulation

## Slide 22: Distance Sensors (Phase)

## Slide 23: Distance Sensors (Triangulation)

## Slide 24: C Program Structure

## Slide 25: C Grammar: “if” Clause

## Slide 26: C Grammar: “while” Clause

## Slide 27: C Grammar: “for” Clause

## Slide 28: Sample Arduino Code

## Slide 29: Sample Arduino Code

## Slide 30: Sample Arduino Code

## Slide 31: Sample Arduino Code

## Slide 32: Grading
100 points, 20% towards the final grade
  50 points for basic functions
    Moving forward and backward (10 points)
    Turning left and right (10 points)
    Adjusting motion speed (10 points)
    Detecting and avoiding walls and obstacles (10 points)
    Recognizing signs on the wall (10 points)
  50 points for going through the maze, otherwise grading based on its travel distance